## Slide 1
Research Center for Earth Operative Monitoring (NTs OMZ)
  Established in 1999
Operator of Russian Earth observation satellites

## Slide 2
  Systematic and applied research
  Development of ground EO infrastructure segments
  Analytics/consulting
  Satellite acquisitions planning
  Participation in satellites tasking
  Exploitation of ETRIS DZZ system
  Data reception
  Data processing
  Data quality control
  Data storage
  Federal data fund
  Geoportal of State Space Corporation “Roscosmos”
Main activities
  Main customers –
  State Space Corporation “Roscosmos” and space organizations
  Orbital constellation
  Ground infrastructure
  Science and technologies
  Information sources

## Slide 3
Space monitoring
GLOBAL
REGIONAL
LOCAL
Meteor-M
Electro-L
Arktika-M
Resurs-P
Kanopus-V
Hydrometeorological observation
Low resolution (lower than 1 000 m) – free access
Acquisition – each 30 minutes
Environmental and resource monitoring
Disasters management
High and medium resolution (15 – 1 000 m) – free access
Daily revisit period
Infrastructure monitoring
mapping
Detailed and high resolution (0.7 – 15 m) – free access for governmental authorities
Daily revisit period
Meteor-M
Resurs-P
Kanopus-V-IK

## Slide 4
RESURS-P and KANOPUS-V
PURPOSE
Acquisition of high resolution EO data in visible and IR spectra for environment monitoring, natural resources inventory, raw materials search, large-scale mapping.
RESURS-P, SENSORS
Optical electronic VHR sensor [Geoton]
  Panchromatic resolution
  (0.60-0.72 μm) – 0.9 m
  Multispectral resolution
  (5 bands, 0.45-0.90 μm) – 3 m
  Swath width – 38 km
Wide-band multispectral HR sensor [ShMSA-VR]
  Panchromatic resolution
  (0.58-0.80 μm) – 12 m
  Multispectral resolution
  (5 bands, 0.43-0.90 μm) – 23.8 m
  Swath width – 97 km
  1 satellite, orbit time – 94.07 min, AOI revisit period – 3 days
Wide-band multispectral MR sensor [ShMSA-SR]
  Panchromatic resolution
  (0.58-0.80 μm) – 60 m
  Multispectral resolution
  (5 bands, 0.43-0.90 μm) – 120 m
  Swath width – 441 km
  Hyperspectral sensor [GSA]
  Resolution (up to 255 bands, 0.4-0.9 μm) – 30 m
  Swath width – 25 km
KANOPUS-V, SENSORS
Panchromatic acquisition system [PSS]
  Resolution (0.54-0.86 μm) – 2.1 m
Swath width – 23 km
Multispectral acquisition system [MSS]
  Resolution (4 bands, 0.46-0.84 μm) – 12 m
Swath width – 20 km
  5 satellites, orbit time – 94,74 мин
  AOI revisit period – 1-2 days due to the amount of constellation satellites
Multi-zone IR scanner [MSU-IK-SRM] – Kanopus-V-IK
  Resolution (2 bands: 3.5-4.5, 8.4-9.4 μm) – 200 m
Swath width – 2,000 km
Noise equivalent of measured temperatures difference at 300 K – 0.1-0.2 К
Minimum size of detectable fire spot – 5×5 m

## Slide 5
RESURS-P

## Slide 6
RESURS-P

## Slide 7
KANOPUS-V

## Slide 8
METEOR-М, ELECTRO-L, ARKTIKA-M
PURPOSE
Operative data acquisition on cloud coverage and underlying surface condition, hydrometeorological data acquisition and measurements, helio-physical research, environmental monitoring, Arctic region monitoring
METEOR-M, SENSORS
  Multi-zone satellite acquisition complex [KMSS]
Multi-zone scanner [MSU-100]
  Multispectral resolution
  (3 bands, 0.53-0.90 μm) – 60 m
  Swath width – 900 km
Multi-zone scanner [MSU-50]
  Multispectral resolution
  (3 bands, 0.37-0.69 μm) – 120 m
  Swath width – 900 km
  Multi-zone LR scanner [MSU-MR]
  Multispectral resolution
  (6 bands, 0.5-12.5 μm) – 1000 m
  Swath width – 2800 km
  3 satellites, revisit period:
  MSU – entire Earth’s surface twice a day;
  KMSS – covers AOI once per 3 days
  Helio-physical hardware complex
  [GGAK]
ELECTRO-L, SENSORS
  Multi-zone scanner [MSU-GS]
  Covered territory – visible Earth disk
  Resolution in visible specter (3 bands: 0.46–0.90 μm) – 1000 m
  Near-IR resolution (7 bands: 3.5-12.5 μm) – 4000 m
  2 satellites, revisit period – 30 min (standard)
  – 15 min (upon request)
ARKTIKA-M, SENSORS
  Multi-zone scanner [MSU-GS]
  Covered territory – Arctic region
  Resolution in visible specter (3 bands: 0.50-0.90 μm) – 1000 m
  Near-IR resolution (7 bands: 3.5-12.5 μm) – 4000 m
  1 satellite, revisit period – 30 min (standard)
  – 15 min (upon request)

## Slide 9
METEOR-M

## Slide 10
ELECTRO-L
Visible bands (RGB)
IR band (10,2-11,2µm)

## Slide 11
ARKTIKA-M
Visible bands (RGB)
IR band (10,2-11,2µm)

## Slide 12
Ground EO infrastructure
More than 300 specialists working 24/7
16 data reception centers (11 – Roscosmos, 5 – Roshydromet)
64 antenna complexes (43 – Roscosmos, 21 – Roshydromet)

## Slide 13
данных
данных
Federal and regional authorities
Geoportal
EO satellite information
Main stages of EO data processing in NTs OMZ
Legal entities
Acquisition tasking
Data order from EO data state fund
Acquisition data
Data from EO data state fund
API
Services
Physical entities
Radiometric correction
Geometric correction
Atmospheric correction
Quality control
Insertion into databank
Publishing on portal
*APOI– automated stream processing of information
APOI*
Databank

## Slide 14
Thank you for your attention!
Research Center for Earth Operative Monitoring (NTs OMZ)
Official website: www.ntsomz.ru